## Slide 1: HSUV Example Change Scenario
Step by step discussion of how the requirements change scenario plays out in the example model

## Slide 2: Preconditions
HSUV model including requirements and structure elements exists
Model elements are at initial versions
Model is fully “released”
  Locked so no edits can be done without creating a new version

## Slide 3: Step 1 – Change Requirements to 2016 ULEV
Marketing opens change request
  Need to change vehicle to meet 2016 ULEV standards
  Change request has problem item REQ-000144/A attached
  Change request has reference item AMG54556/001 attached (this is the total product context, unconfigured for this step)
Released REQ-000144/A is revised to begin work on version “B”
When version “B” is finished it is released, then next higher assembly (REQ-000181/A) is revised to include this new version, and released
  Same sequence for each level to the top of the requirements tree (AKY251614/001 becomes AKY251614/002)
  Revise the product context (AMG54556/001, swap in the new version of the requirements (AKY251614/002), but do not yet release it, since the design must also be changed
Postcondition – Released context now has AKY251614/002, REQ-000181/B, REQ-000144/B, AMG54556/002 is in working state, rest are not changed.

## Slide 4: Step 2 – Change Design to Meet Revised Requirements
Original change request remains open, related structure items must be fixed to meet the revised requirement
  Follow the <<satisfy>> link from REQ-000144/A to find PowerSubsystem AMG60104/001, add it to the list of problem items on the change request
  Revise released AMG60104/001 to version 002 and begin changes to meet new requirement
  Create new versions of PowerControlUnit, FuelTankAssembly, ApplicationSoftware and Calibrations to meet new requirement
    Attach each original version to the change request as problem items (NOTE: This could have been done when the initial change request was created by following the links from the requirement that was attached)
    Attach the revised versions as solution items
    NOTE: ApplicationSoftware and Calibrations should probably be further decomposed and the change should roll down to internal items inside them, such as a specific version of a specific software component, etc. to illustrate the ALM connectivity to the context
  Release all the new versions, replace original versions in AMG60104/002 and release it
  Change top structure HybridSUV assembly (AMG60112/001) to include new PowerSubsystem version and release it
  Swap the new version into the working version of the product context (AMG54556/002) and release it
Close the change request as complete
  This step may be automatic based on how the change request system is configured to handle closing of the change based on release of the solution items.

## Slide 5: Step 3 – Change Requirements to add Variant for EU
Marketing opens change request
  Need to change vehicle to meet 2016 ULEV standards in two different markets, US and EU, using two variants
  Change request has problem item REQ-000144/B attached
  Change request has reference item AMG54556/002 attached (this is the product context, configuration options are to be added in this step)
Released REQ-000144/B is OK as written so no change
The next higher assembly (REQ-000181/B) must be revised to add the variant expression on the two instances of the REQ-000144/B requirement, one for each of US and EU markets
  The top requirement context must be revised to include the new variant enabled REQ-000181/C (AKY251614/002)
  Product context must be setup to expose the US or EU region option to be set (AMG54556/002)
Postcondition – Released requirements context now has AKY251614/003 and REQ-000181/C, AMG54556/002 is in working status, rest are not changed.

## Slide 6: Step 4 – Change Design to Meet Revised Requirements
NOTE: This change request cannot be cleanly handled with current Teamcenter (v8.3.0.3), the links are not in context of the usage so there cannot be two different destination items based on the variant of REQ-000144/B selected
Original change request remains open, related structure items must be fixed to meet the revised requirement
  Follow the <<satisfy>> link from REQ-000144/B to find PowerSubsystem AMG60104/002, add it to the list of problem items on the change request
  Revise released AMG60104/002 to version 003 and begin changes to meet new requirement
  Create new versions of PowerControlUnit, ApplicationSoftware and Calibrations to meet new requirement
    Attach each original version to the change request as problem items (NOTE: This could have been done when the initial change request was created by following the links from the requirement that was attached)
    Attach the revised versions as solution items
    To simulate the capability to have links in context of a view, we need to create same options and variant expressions here as in the requirements tree to allow the configuration to make correct selections
  Release all the new versions, replace original versions in AMG60104/003 and release it
  Change top structure HybridSUV assembly (AMG60112/002) to include new PowerSubsystem version and release it
  Swap the new version into the working version of the product context (AMG54556/003) and release it
Close the change request as complete
  This step may be automatic based on how the change request system is configured to handle closing of the change based on release of the solution items.

## Slide 7: Key Configuration Capabilities of the Model
Revision Effectivity
  In process while a change is taking place, part of the model is in a state of change, other parts are in released state
  Revision effectivity can return both the current working version of the complete model as well as the currently released version of the model
Variant Effectivity
  Variant effectivity can return the model configured to represent either the US variant or the EU variant
Baselines
  A baseline in PLM is a special locked (released) version that cannot be further changed (a “stubbed branch”)